## Slide 1
FIRE
BOT
Bluetooth Fire-Fighting Robot
HC-05 Bluetooth
Arduino Nano
Web Serial API
L298N Motor Driver
Working Principle & System Architecture

## Slide 2
SYSTEM OVERVIEW
Key components and how they connect
💻 CONTROLLER
Chrome / Edge browser
Web Serial API
Bluetooth HTML UI
Real-time CMD send
⚙️ ROBOT BRAIN
Arduino Nano / Uno
HC-05 Bluetooth
L298N Motor Driver
Servo + Relay
🔥 SENSORS
Flame sensor (digital)
DHT11 Temperature
HC-SR04 Ultrasonic
Live data to UI
⟶
CMD
Bluetooth
⟶
DATA
Sensors

## Slide 3
COMMUNICATION FLOW
HC-05 Bluetooth ↔ Web Serial API ↔ Arduino
🖥️
Browser UI
Chrome / Edge
Web Serial API
1
▶
📡
HC-05 Module
Paired via Windows
Bluetooth Settings
2
▶
🤖
Arduino
9600 baud
Hardware Serial
3
▶
⚡
Actuators
Motors / Pump
Servo / LEDs
4
COMMAND PROTOCOL
F / B / L / R
Movement commands
S
Emergency stop
SPD:150
Set PWM speed 0–255
P1 / P0
Pump ON / OFF
FLAME:1 TEMP:28 DIST:35
Sensor data (every 500ms)

## Slide 4
MOTOR CONTROL
L298N H-Bridge driver with PWM speed control
Command
IN1
IN2
IN3
IN4
ENA/B
Result
F — Forward
HIGH
LOW
HIGH
LOW
PWM
Both motors forward
B — Backward
LOW
HIGH
LOW
HIGH
PWM
Both motors reverse
L — Left
LOW
HIGH
HIGH
LOW
PWM
Left back, Right fwd
R — Right
HIGH
LOW
LOW
HIGH
PWM
Left fwd, Right back
S — Stop
LOW
LOW
LOW
LOW
0
All motors off
SPEED
CONTROL
255
100%
200
78%
150
59%
100
39%
0
0%
Motor speed sent as SPD:N (0–255 PWM). Auto-stop command (S) issued on button release or page close.

## Slide 5
SENSOR SYSTEM
Three sensors broadcast live data to the browser every 500 ms
🔥 FLAME SENSOR
PIN
Pin 8 (Digital)
HOW IT WORKS
Detects IR radiation from fire. Outputs LOW when flame present.
DATA FORMAT
FLAME:1 (fire) or FLAME:0 (clear)
UI ACTION
Triggers alarm banner in UI. Auto mode activates pump.
🌡️ DHT11 TEMP
PIN
Pin 3 (1-Wire)
HOW IT WORKS
Measures ambient temperature using capacitive humidity + NTC thermistor.
DATA FORMAT
TEMP:28.4 (°C, 1 decimal)
UI ACTION
Displayed live in sensor panel. No auto-action.
📡 HC-SR04 ULTRASONIC
PIN
Trig:12 / Echo:13
HOW IT WORKS
Sends 40kHz pulse, measures echo return time → distance in cm.
DATA FORMAT
DIST:35 (cm, integer)
UI ACTION
Auto mode avoids obstacles < 20 cm. Displayed in UI.
Arduino broadcasts →
FLAME:1 TEMP:28.4 DIST:35
every 500 ms

## Slide 6
FIRE FIGHTING LOGIC
Manual control + Auto mode decision tree
🕹️ MANUAL CONTROLS
💧
Water Pump
Toggle relay on pump motor
P1 / P0
🔄
Servo Sweep
Oscillates nozzle 45°→135°
V1 / V0
🔔
Alarm Buzzer
Audible fire alert signal
Z1 / Z0
💡
Headlights
Front LED illumination
D1 / D0
🤖 AUTO MODE FLOW
Read Sensors
(Flame + Distance)
▼
Flame = 1?
OR Dist < 20cm?
YES ▶
NO ▶
FLAME: Pump ON + Buzzer ON
OBSTACLE: Reverse → Turn Right
Drive Forward
Continue patrol
↺ Repeats every 150 ms

## Slide 7
BROWSER UI BREAKDOWN
HTML + Web Serial API — Chrome / Edge on laptop
Connect Screen
Baud rate selector (9600–115200). requestPort() opens COM port. Spinner during handshake.
D-Pad Controls
Pointer + keyboard events (↑↓←→ Space). Sends on press, stops on release. No command flooding.
Speed Slider
PWM 0–255 range input. Sends SPD:N on every change. Live % and PWM display.
Sensor Panel
Regex parses FLAME / TEMP / DIST from each incoming line. Alert banner on flame.
Serial Monitor
200-line rolling log. TX in red, RX in green. TX/RX counters. Autoscroll toggle.
⚠ KEY FIXES IN THIS VERSION
✖ Writer Lock Bug
✔ Single persistent writer held open. No getWriter() per command.
✖ Key Repeat Flooding
✔ heldKeys Set prevents duplicate sends while key is held down.
✖ No Auto-Stop
✔ beforeunload event sends 'S' when tab/window is closed.
✖ Disconnection Crash
✔ Read-loop catch shows reconnect overlay instead of silent fail.
✖ Hardcoded Baud Rate
✔ Dropdown selector: 9600 / 19200 / 38400 / 57600 / 115200.

## Slide 8
PIN MAP & WIRING
Arduino Nano / Uno — connect these before uploading the sketch
Motor Driver (L298N)
IN1
→ 4
Left motor dir A
IN2
→ 5
Left motor dir B
IN3
→ 6
Right motor dir A
IN4
→ 7
Right motor dir B
ENA
→ 10 (PWM)
Left speed
ENB
→ 11 (PWM)
Right speed
Sensors
Flame
→ 8
Digital — LOW=fire
Trig
→ 12
HC-SR04 trigger
Echo
→ 13
HC-SR04 echo
DHT11
→ 3
Temp sensor data
Actuators
Pump relay
→ A0
Water pump
Servo
→ 9 (PWM)
Nozzle servo
Buzzer
→ A1
Alarm
LEDs
→ A2
Headlights
⚠ HC-05 → Arduino RX (pin 0) & TX (pin 1) via 5V↔3.3V voltage divider. UNPLUG HC-05 before uploading sketch — it shares the hardware Serial port!

## Slide 9
HOW TO RUN
Step-by-step setup from zero to driving
01
Install Libraries
In Arduino IDE: Sketch → Manage Libraries → Install 'DHT sensor library' by Adafruit. Servo is built-in.
02
Upload Sketch
Unplug HC-05 TX/RX wires. Open firebot_arduino.ino, select correct board & port, click Upload. Replug HC-05.
03
Pair Bluetooth
Windows Settings → Bluetooth → Add device → Select HC-05. Default PIN: 1234 or 0000. Note the COM port assigned.
04
Open HTML Controller
Open firebot_bluetooth.html in Chrome or Edge. Click 'Connect via Bluetooth', select the HC-05 COM port.
05
Control!
Use D-pad, keyboard arrows, speed slider, pump and extras. Watch sensor data update live in the UI.

## Slide 10
SUMMARY
6
Commands
Supported
3
Live Sensors
Streamed
500ms
Sensor
Broadcast Rate
9600
HC-05 Baud
Rate (default)
KEY TAKEAWAYS
Web Serial API replaces native apps — full Bluetooth control in a browser tab
Single persistent writer eliminates lock contention bugs on rapid command send
Arduino broadcasts sensor telemetry every 500 ms — UI parses with regex
Auto mode handles obstacle avoidance + fire suppression without UI input
Auto-stop on page close ensures robot never drives away if tab crashes
FireBot — Bluetooth Fire Fighting Robot | Arduino + HC-05 + Web Serial